## Slide 1: Time-Resolved STED Microscopy
Giuseppe Vicidomini giuseppe.vicidomini@iit.it
@VicidominiLab
Molecular Microscopy and Spectroscopy Istituto Italiano di Tecnologia, Genoa
Photo: Paolo Bianchini
IIT, Genoa, Italy
6 December 2019

## Slide 2
Introduction

## Slide 3: Fluorescence Microscopy
3
“…..Browse through any cell biological journal, and the impact of fluorescent microscopy is obvious, with > 80% of the images of cells in the book usually acquired with a fluorescent microscope……“
B. Houng et al. Cell 143:1047-1058 (2010)
3RD PLACE, 2012 PHOTOMICROGRAPHY COMPETITION
Dr. Dylan T. Burnette, National Institutes of Health (NIH),Bethesda, Maryland, USA
Human bone cancer (osteosarcoma) showing actin filaments (purple), mitochondria (yellow), and DNA (blue).
Notes: You may be surprise to know that more than 80% of the images of cell in a biological journal or book have been acquired using a fluorescent microscope.

## Slide 4: Fluorescence Microscopy
4
“…..Browse through any cell biological journal, and the impact of fluorescent microscopy is obvious, with > 80% of the images of cells in the book usually acquired with a fluorescent microscope……“
B. Houng et al. Cell 143:1047-1058 (2010)
3RD PLACE, 2012 PHOTOMICROGRAPHY COMPETITION
Dr. Dylan T. Burnette, National Institutes of Health (NIH),Bethesda, Maryland, USA
Human bone cancer (osteosarcoma) showing actin filaments (purple), mitochondria (yellow), and DNA (blue).
L. Schermelleh et al. JCB 190(2): 165-175 (2010)
non-invasive
Notes: This great success stems from the unique characteristics offered by fluorescente microscopy.
Probably the most important is the possibility to make imaging in the physiological conditions for the sample

## Slide 5: Fluorescence Microscopy
5
“…..Browse through any cell biological journal, and the impact of fluorescent microscopy is obvious, with > 80% of the images of cells in the book usually acquired with a fluorescent microscope……“
B. Houng et al. Cell 143:1047-1058 (2010)
3RD PLACE, 2012 PHOTOMICROGRAPHY COMPETITION
Dr. Dylan T. Burnette, National Institutes of Health (NIH),Bethesda, Maryland, USA
Human bone cancer (osteosarcoma) showing actin filaments (purple), mitochondria (yellow), and DNA (blue).
L. Schermelleh et al. JCB 190(2): 165-175 (2010)
non-invasive
three-dimensional (x,y,z)
multi-color (𝜆)
time-series (t)

## Slide 6: Fluorescence Microscopy
6
“…..Browse through any cell biological journal, and the impact of fluorescent microscopy is obvious, with > 80% of the images of cells in the book usually acquired with a fluorescent microscope……“
B. Houng et al. Cell 143:1047-1058 (2010)
3RD PLACE, 2012 PHOTOMICROGRAPHY COMPETITION
Dr. Dylan T. Burnette, National Institutes of Health (NIH),Bethesda, Maryland, USA
Human bone cancer (osteosarcoma) showing actin filaments (purple), mitochondria (yellow), and DNA (blue).
L. Schermelleh et al. JCB 190(2): 165-175 (2010)
non-invasive
three-dimensional (x,y,z)
multi-color (𝜆)
time-series (t)
system complexity
sample preparation
artefact free

## Slide 7: Fluorescence Microscopy
7
“…..Browse through any cell biological journal, and the impact of fluorescent microscopy is obvious, with > 80% of the images of cells in the book usually acquired with a fluorescent microscope……“
B. Houng et al. Cell 143:1047-1058 (2010)
3RD PLACE, 2012 PHOTOMICROGRAPHY COMPETITION
Dr. Dylan T. Burnette, National Institutes of Health (NIH),Bethesda, Maryland, USA
Human bone cancer (osteosarcoma) showing actin filaments (purple), mitochondria (yellow), and DNA (blue).
L. Schermelleh et al. JCB 190(2): 165-175 (2010)
non-invasive
three-dimensional (x,y,z)
multi-color (𝜆)
time-series (t)
system complexity
sample preparation
artefact free
spatial resolution
Notes: Finally, conventional fluorescent microscopy provides a

## Slide 8: Diffraction Barrier
8
Illustration: © Johan Jarnestad
The Royal Swedish Academy of Sciences
Fluorescence Microscopy
Naked Eye
Electron Microscopy

## Slide 9: Diffraction Barrier
9
Illustration: © Johan Jarnestad
The Royal Swedish Academy of Sciences
Electron Microscopy
Super-Resolved Fluorescence Microscopy (or Nanoscopy)
Naked Eye
Notes: Among all the super-resolved microscope STED microscopy, invented in 1994 from Prof. Stefan Hell, from a initial scepticism is nowadays gaining a substantial momentum.

## Slide 10: Stimulated Emission Depletion (STED) Microscopy
10

## Slide 11
Basic Fluorescence

## Slide 12: Fluorescence
12
S0
S1
Simplified Jablonski
Diagram
}
vibrational
states
}
vibrational
states
Excitation: absorption of a photon whose energies match with the molecule (10-15 s)

## Slide 13: Fluorescence
13
S0
S1
Simplified Jablonski
Diagram
}
vibrational
states
}
vibrational
states
Excitation: absorption of a photon whose energies match with the molecule (10-15 s)
Vibrational Relaxation: relaxation to the lower vibrational level of the excited state (10-12 s)

## Slide 14: Fluorescence
14
S0
S1
Simplified Jablonski
Diagram
}
vibrational
states
}
vibrational
states
Excitation: absorption of a photon whose energies match with the molecule (10-15 s)
Vibrational Relaxation: relaxation to the lower vibrational level of the excited state (10-12 s)
Fluorescent (Spontaneous) Emission: emission (10-15 s) of a photons at higher wavelength. Excited state lifetime (10-9 s)

## Slide 15: Fluorescence
15
S0
S1
Simplified Jablonski
Diagram
}
vibrational
states
}
vibrational
states
Excitation: absorption of a photon whose energies match with the molecule (10-15 s)
Vibrational Relaxation: relaxation to the lower vibrational level of the excited state (10-12 s)
Fluorescent (Spontaneous) Emission: emission (10-15 s) of a photons at higher wavelength. Excited state lifetime (10-9 s)
Stimulated Emission: emission of an identical photon by providing a second stimulating photon

## Slide 16
STED Microscopy
Notes: With this bases of fluorescence

## Slide 17: Diffraction (in a Laser Scanning Microscope)
17
d= 𝛌/(2*NA)
  Abbe E., Mikroscopische Anatomie 9:413-468 (1873)
Notes: How a STED microscope work? To understand how a STED microscope is able to reach sub diffraction spatial resolution it is necessary to understand why diffraction limits the resolution of a conventional fluorescence scanning microscope.

## Slide 18: Diffraction (in a Laser Scanning Microscope)
18
d= 𝛌/(2*NA)
  Abbe E., Mikroscopische Anatomie 9:413-468 (1873)

## Slide 19: Diffraction (in a Laser Scanning Microscope)
19
d= 𝛌/(2*NA)
  Abbe E., Mikroscopische Anatomie 9:413-468 (1873)

## Slide 20: Diffraction (in a Laser Scanning Microscope)
20
d= 𝛌/(2*NA)
  Abbe E., Mikroscopische Anatomie 9:413-468 (1873)

## Slide 21: Diffraction (in a Laser Scanning Microscope)
21
d= 𝛌/(2*NA)
  Abbe E., Mikroscopische Anatomie 9:413-468 (1873)

## Slide 22: Diffraction (in a Laser Scanning Microscope)
22
d= 𝛌/(2*NA)
  Abbe E., Mikroscopische Anatomie 9:413-468 (1873)

## Slide 23: Diffraction (in a Laser Scanning Microscope)
23
d= 𝛌/(2*NA)
  Abbe E., Mikroscopische Anatomie 9:413-468 (1873)
Vicidomini G.,…, Diaspro A., Methods, 66 (2), 124-130 (2014)
Notes: Clearly, if there is a method to prevent the “simultaneous” emission from adjacent (closer to the diffraction limit) fluorophores, the spatial resolution of the system will be enhanced.

## Slide 24: STED Microscopy
24
  Hell S.W. and Wichmann J., Opt. Lett. 19, 780–782 (1994)
  Vicidomini G.,…, Diaspro A., Nat,. Methods, 15:173–182 (2018)
Vicidomini G.,…, Diaspro A., Methods, 66 (2), 124-130 (2014)

## Slide 25: STED Microscopy
25
Vicidomini G.,…, Diaspro A., Methods, 66 (2), 124-130 (2014)
  Hell S.W. and Wichmann J., Opt. Lett. 19, 780–782 (1994)
  Vicidomini G.,…, Diaspro A., Nat,. Methods, 15:173–182 (2018)

## Slide 26: STED Microscopy
26
Vicidomini G.,…, Diaspro A., Methods, 66 (2), 124-130 (2014)
OFF
ON
  Hell S.W. and Wichmann J., Opt. Lett. 19, 780–782 (1994)
  Vicidomini G.,…, Diaspro A., Nat,. Methods, 15:173–182 (2018)

## Slide 27: STED Microscopy
27
d= 𝛌/(2*NA*√(1+ImSTED))
Vicidomini G.,…, Diaspro A., Methods, 66 (2), 124-130 (2014)
OFF
ON
OFF
ON
  Hell S.W. and Wichmann J., Opt. Lett. 19, 780–782 (1994)
  Vicidomini G.,…, Diaspro A., Nat,. Methods, 15:173–182 (2018)

## Slide 28: STED Microscopy
28
d= 𝛌/(2*NA*√(1+ImSTED))
OFF
ON
Vicidomini G.,…, Diaspro A., Methods, 66 (2), 124-130 (2014)
OFF
ON
  Hell S.W. and Wichmann J., Opt. Lett. 19, 780–782 (1994)
  Vicidomini G.,…, Diaspro A., Nat,. Methods, 15:173–182 (2018)

## Slide 29: STED Conditions
29
Spatial condition: the STED beam and the excitation beam foci have to coincide with nanometres precision and the residual STED beam’s intensity in the “zero”-intensity point has to be minimised
Galiani, S.,…, Bianchini, P., Opt. Express, 20(7):7362-7374 (2012)
  Vicidomini G.,…, Diaspro A., Nat,. Methods, 15:173–182 (2018)

## Slide 30: STED Conditions
30
Rankin B.R.,…, Hell S.W., Biophys. J., 100, L63-L65 (2011)
Spatial condition: the STED beam and the excitation beam foci have to coincide with nanometres precision and the residual STED beam’s intensity in the “zero”-intensity point has to be minimised
Spectral condition: the STED beam wavelength has to be chosen to maximise stimulated emission and minimise fluorophore absorption
Galiani, S.,…, Bianchini, P., Opt. Express, 20(7):7362-7374 (2012)
  Vicidomini G.,…, Diaspro A., Nat,. Methods, 15:173–182 (2018)

## Slide 31: Spectral Conditions
31
The wavelength of the STED beam is set to maximise the quenching of the excited fluorophores via stimulated emission and to minimise any other processes that can compete
with stimulated emission
Castello M.,…, Vicidomini G., Review of Sci. Instr,, In Press

## Slide 32: Spectral Conditions
32
The wavelength of the STED beam is set to maximise the quenching of the excited fluorophores via stimulated emission and to minimise any other processes that can compete
with stimulated emission
Castello M.,…, Vicidomini G., Review of Sci. Instr,, In Press

## Slide 33: Spectral Conditions
33
The wavelength of the STED beam is set to maximise the quenching of the excited fluorophores via stimulated emission and to minimise any other processes that can compete
with stimulated emission
Rankin B.R,…, Hell S.W., Biophys. J., 100, L63-L65 (2011)
green
fluoresce
protein
(GFP)
Castello M.,…, Vicidomini G., Review of Sci. Instr,, In Press
Photobleaching reduces by choosing wavelength of the STED beam outside the excited-state absorption spectra,

## Slide 34: Spectral Conditions
34
The wavelength of the STED beam is set to maximise the quenching of the excited fluorophores via stimulated emission and to minimise any other processes that can compete
with stimulated emission
Rankin B.R,…, Hell S.W., Biophys. J., 100, L63-L65 (2011)
green
fluoresce
protein
(GFP)
Castello M.,…, Vicidomini G., Review of Sci. Instr,, In Press
Photobleaching reduces by choosing wavelength of the STED beam outside the excited-state absorption spectra,
but - red-shifting the STED beam reduces the stimulated emission cross section; - blu-shifting the STED beam increases the probability to excite directly the fluorophore.

## Slide 35
Sync-STED Microscopy

## Slide 36: Synchronous STED
36
If the absorption of the STED beam is not negligible a background (anti-Stokes emission background) substantially reduces the effective spatial resolution.
Confocal
CW-STED
CW-STED
Confocal
CW-STED

## Slide 37: Synchronous STED
37
If the absorption of the STED beam is not negligible a background (anti-Stokes emission background) substantially reduces the effective spatial resolution.
The anti-Stokes emission background cannot be spectrally filtered but since it is induced solely by the STED beam it can be removed by a lock-in (synchronous detection) approach
CW-STED (sync)
excitation
STED
open
close
Digital lock-in (syncrounous detection) directly integrated in the microscope data-acquisition card (FPGA-based)
time
pixel dwell-time
Castello M.,…, Vicidomini G., Review of Sci. Instr,, 88, 053701 (2017)
-
=
CW-STED
Confocal
(sync)

## Slide 38: Anti-Stokes Emission Background Removal
38
Castello M.,…, Vicidomini G., Review of Sci. Instr., 88, 053701 (2017)
The excitation beam is modulated and the uncorrelated anti-Stokes emission background is “subtracted” (the background from early emission is also removed integrating the approaches in a time-resolved STED architecture):
      Vicidomini G. et al. Opt. Express, 20:5225–5236 (2012)
      Ronzitti E. et al. Opt. Express 21:210–219 (2013)
      Hernandez I.C. et al. J. Biophoton. 7:376–80 (2014)
      Hanne J. et al. Nat. Commun. 6:7127 (2015)
      Lanzanò L. et al. Nat. Commun. 6:6701 (2015)
      Castello M. et al. Review of Sci. Instr. 88:053701 (2017)
The anti-Stokes emission background is “subtracted" via image deconvolution to improve the SNR:
      Hernandez I.C. et al. Sci. Rep. 6:19419 (2016) Castello M. et al. Review of Sci. Instr. 88:053701 (2017)
      Hernandez. I.C. et al. Neurophotonics 6:045004 (2019)
The background from incomplete depletion is also removed:
      Gao P. et al. Nature Photon 11:163–169 (2017)
      Lee J.C. et al. ACS Photonics 6:1789-1797 (2019)
A recent review on this topic Ma Y., et al. Phys. Biol. 16:051002 (2019)

## Slide 39: STED Conditions (Temporal)
39
Rankin B.R.,…, Hell S.W., Biophys. J., 100, L63-L65 (2011)
Spatial condition: the STED beam and the excitation beam foci have to coincide with nanometres precision and the residual STED beam’s intensity in the “zero”-intensity point has to be minimised
Spectral condition: the STED beam wavelength has to be chosen to maximise stimulated emission and minimise fluorophore absorption
Temporal condition: the STED beam photons (stimulating photons) have to act when fluorophores are in the singlet-excited state S1
Vicidomini, G.,…, Hell, S.W., PLoS ONE, 8(1):e54421 (2013)
Galiani, S.,…, Bianchini, P., Opt. Express, 20(7):7362-7374 (2012)
  Vicidomini G.,…, Diaspro A., Nat,. Methods, 15:173–182 (2018)

## Slide 40: Temporal Conditions
40
The depletion of the fluorescent signal depends on the number of stimulating photons to which the fluorophore is exposed while residing in the singlet-excited state S1
stimulated emission photon cross-section 𝜎SE = 25 cm2/J
excited-state S1 lifetime 𝜏S1 = 4 ns
Isat = 10 MW/cm2
ImSTED ~ GW/cm2
complex pulsed lasers architecture
photo-damage effects
~ ns
~ ps
S0
S1
Notes: The reason why the stimulating photons have to act when fluorophores are in the singlet-excited state S1, is because the suppression of fluorescence depends on the number of stimulating photons to which the fluorophore is exposed while residing in the excite-state.
However, since typically organic fluorophores have lifetime in the order of nanoseconds and the crosse section of stimulate at the STED beam wavelength is relatively low, Intensity of the STED beam of the order of GW/cm2 are requested to effectively reach tens of nanometer resolutions
For this reason the most natural way to efficiently quench a fluorophore is to synchronise the excitation events with the stimulating photons which can be achieved with a train of synchronised excitation and stimulating pulses, in which the stimulating pulse follows instantaneously the excitation pulse.
For organic fluorophore with a lifetime of few nanoseconds, hundreds picosecond stimulating pulse (i) ensures that all the stimulating photons acts while the fluorophore is in the excited state, allows (ii) to the fluorophore to relax from the vibrational states.
However, since stimulated emission cross-section is in the order of 𝜎SE = 10-16cm2, also with few hundreds picosecond pulses the peak intensity to effectively quench a fluorohore is in the order of GW/cm2.
Clearly, this value is well above the intensity values used to excite the fluorophores (below the intensity use in two-photon-excitation) thus prone to induce photo-bleaching and photo-toxicity in living sample.

## Slide 41: Temporal Conditions
41
The depletion of the fluorescent signal depends on the number of stimulating photons to which the fluorophore is exposed while residing in the singlet-excited state S1
stimulated emission photon cross-section 𝜎SE = 25 cm2/J
excited-state S1 lifetime 𝜏S1 = 4 ns
Isat = 10 MW/cm2
ImSTED ~ GW/cm2
complex pulsed lasers architecture
photo-damage effects
~ ns
~ ps
S0
S1
- long lifetime fluorophores;
Notes: The suppression of fluorescence depends on the number of stimulating photons to which the fluorophore is exposed while residing in the excite-state.
For this reason the most natural way to efficiently quench a fluorophore is to synchronise the excitation events with the stimulating photons which can be achieved with a train of synchronised excitation and stimulating pulses, in which the stimulating pulse follows instantaneously the excitation pulse.
For organic fluorophore with a lifetime of few nanoseconds, hundreds picosecond stimulating pulse (i) ensures that all the stimulating photons acts while the fluorophore is in the excited state, allows (ii) to the fluorophore to relax from the vibrational states.
However, since stimulated emission cross-section is in the order of 𝜎SE = 10-16cm2, also with few hundreds picosecond pulses the peak intensity to effectively quench a fluorohore is in the order of GW/cm2.
Clearly, this value is well above the intensity values used to excite the fluorophores (below the intensity use in two-photon-excitation) thus prone to induce photo-bleaching and photo-toxicity in living sample.

## Slide 42: Temporal Conditions
42
The depletion of the fluorescent signal depends on the number of stimulating photons to which the fluorophore is exposed while residing in the singlet-excited state S1
- long lifetime fluorophores;
time-gating detection: registering fluorescence signal only after a certain time Tg from the fluorophores’ excitation events ensures that the signal stems fromfluorophores that have resided into the excited-state at least a time Tg
stimulated emission photon cross-section 𝜎SE = 25 cm2/J
excited-state S1 lifetime 𝜏S1 = 4 ns
Isat = 10 MW/cm2
ImSTED ~ GW/cm2
complex pulsed lasers architecture
photo-damage effects
~ ns
~ ps
S0
S1
Notes: The suppression of fluorescence depends on the number of stimulating photons to which the fluorophore is exposed while residing in the excite-state.-
For this reason the most natural way to efficiently quench a fluorophore is to synchronise the excitation events with the stimulating photons which can be achieved with a train of synchronised excitation and stimulating pulses, in which the stimulating pulse follows instantaneously the excitation pulse.
For organic fluorophore with a lifetime of few nanoseconds, hundreds picosecond stimulating pulse (i) ensures that all the stimulating photons acts while the fluorophore is in the excited state, allows (ii) to the fluorophore to relax from the vibrational states.
However, since stimulated emission cross-section is in the order of 𝜎SE = 10-16cm2, also with few hundreds picosecond pulses the peak intensity to effectively quench a fluorohore is in the order of GW/cm2.
Clearly, this value is well above the intensity values used to excite the fluorophores (below the intensity use in two-photon-excitation) thus prone to induce photo-bleaching and photo-toxicity in living sample.

## Slide 43
gated-STED Microscopy

## Slide 44: Gated-STED Principle
44
Excitation
STED
Detection
Vicidomini G.,…, Hell S.W., PLOS One, 8(1): e544210 (2013)
Moffitt J.R, Osseforth C and Michaelis J. Opt. Express. 19(5):4242-4254 (2011)
~ ns
~ ps
S0
S1
𝜏fl = 1/(kfl+kSTED)
Notes: To understand why time-gating reduces the STED beam intensity requested to obtain a certain sub-diffraction resolution it is necessary to investigate the fluorescent dynamic in a STED experiments.

## Slide 45: Gated-STED Principle
45
Excitation
STED
Detection
Tg
Vicidomini G.,…, Hell S.W., PLOS One, 8(1): e544210 (2013)
Moffitt J.R, Osseforth C and Michaelis J. Opt. Express. 19(5):4242-4254 (2011)
~ ns
~ ps
S0
S1
𝜏fl = 1/(kfl+kSTED)

## Slide 46: Gated-STED Principle
46
Excitation
STED
Detection
Tg
Vicidomini G.,…, Hell S.W., PLOS One, 8(1): e544210 (2013)
Moffitt J.R, Osseforth C and Michaelis J. Opt. Express. 19(5):4242-4254 (2011)
~ ns
~ ps
S0
S1
𝜏fl = 1/(kfl+kSTED)

## Slide 47: Gated-STED Principle
47
Excitation
STED
Detection
Tg
Vicidomini G.,…, Hell S.W., Nat. Methods, 8(7): 571-573 (2011)
Single Nitrogen-Vacancy
Center
~ ns
~ ps
S0
S1

## Slide 48: Gated CW-STED Microscopy
48
Excitation
STED
Detection
Vicidomini G.,…, Hell S.W., PLOS One, 8(1): e544210 (2013)
Moffitt J.R, Osseforth C and Michaelis J. Opt. Express. 19(5):4242-4254 (2011)
Tg
~ ns
~ ps
S0
S1

## Slide 49: Gated CW-STED Microscopy
49
Vicidomini G.,…, Hell S.W., Nat. Methods, 8(7): 571-573 (2011)

## Slide 50: Tune Resolution by Time (or Intensity)
50
Vicidomini G.,…, Diaspro A., Methods, 66 (2), 124-130 (2014)
d= 𝛌/(2*NA*√((1+ImSTED))*(1+Tg))
The resolution improves both with the increase of the STED beam intensity ImSTED and the time-delay Tg

## Slide 51: gCW-STED (features)
51
Vicidomini G.,…, Hell S.W., Nat. Methods, 8(7): 571-573 (2011)
Gated-detection allows to reduce the STED beam power required to obtain sub-diffraction image (200 mW compared to >600 mW)
Increases the photo stability of the fluorophores
Decreases the stress on the sample
(live-cell imaging)

## Slide 52: gCW-STED (features)
52
Gated-detection allows to reduce the STED beam power required to obtain sub-diffraction image (200 mW compared to >600 mW)
Increases the photo stability of the fluorophores
Decreases the stress on the sample
(live-cell imaging)
Confocal
gCW-STED
GFP labeled dense core vesicles moving along axons
ca. 10 µm deep inside an intact anaesthetized drosophila larva.
Courtesy of Prof. Sigrist, FU Berlin, Germany and Leica Microsystems.

## Slide 53: Temporal Conditions
53
The suppression of fluorescence depends on the number of stimulating photons to which the fluorophore is exposed while residing in the excited-state
exc.
STED
time
12.5 ns @ 80 Mhz
300 ps @ 80 Mhz, 𝜏 = 3 ns
stimulated emission cross-section,
𝜎SE = 10-16cm2
STED beam’s intensity,
ISTED = 0.1-1 GW/cm2
~ 1-10 ns
~ 1-10 ps
Notes: The suppression of fluorescence depends on the number of stimulating photons to which the fluorophore is exposed while residing in the excite-state.-
For this reason the most natural way to efficiently quench a fluorophore is to synchronise the excitation events with the stimulating photons which can be achieved with a train of synchronised excitation and stimulating pulses, in which the stimulating pulse follows instantaneously the excitation pulse.
For organic fluorophore with a lifetime of few nanoseconds, hundreds picosecond stimulating pulse (i) ensures that all the stimulating photons acts while the fluorophore is in the excited state, allows (ii) to the fluorophore to relax from the vibrational states.
However, since stimulated emission cross-section is in the order of 𝜎SE = 10-16cm2, also with few hundreds picosecond pulses the peak intensity to effectively quench a fluorohore is in the order of GW/cm2.
Clearly, this value is well above the intensity values used to excite the fluorophores (below the intensity use in two-photon-excitation) thus prone to induce photo-bleaching and photo-toxicity in living sample.

## Slide 54: Temporal Conditions
54
The suppression of fluorescence depends on the number of stimulating photons to which the fluorophore is exposed while residing in the excited-state
exc.
STED
time
1 GW/cm2
300 ps @ 80 Mhz, 𝜏 = 3 ns
200 MW/cm2
1.5 ns @ 80 Mhz, 𝜏 = 3 ns
100 MW/cm2
3 ns @ 80 Mhz, 𝜏 = 3 ns
12.5 ns @ 80 Mhz
peak intensity can be reduced by using
longer pulse, but suppression of fluorescence reduces
stimulated emission cross-section,
𝜎SE = 10-16cm2
STED beam’s intensity,
ISTED = 0.1-1 GW/cm2
~ 1-10 ns
~ 1-10 ps
Notes: Since photobleaching and phytotoxicity mainly depends on the peak intensity, a reduction of the peak intensity is really important to wide the applications of STED microscopy.
Clearly, spreading the stimulating photons on large pulses reduces the peak intensity but also the ability to quench a fluorophore;

## Slide 55: Temporal Conditions
55
The suppression of fluorescence depends on the number of stimulating photons to which the fluorophore is exposed while residing in the excited-state
exc.
STED
time
detection
conventional
time-gating
conventional
time-gating
conventional
time-gating
12.5 ns @ 80 Mhz
stimulated emission cross-section,
𝜎SE = 10-16cm2
STED beam’s intensity,
ISTED = 0.1-1 GW/cm2
peak intensity can be reduced by using
longer pulse, but suppression of fluorescence reduces
the suppression of fluorescence can be fully recovered if the fluorescence is collect only after the action of the STED beam (time-gating detection)
Vicidomini, G.,…, Hell, S.W., PLoS ONE, 8(1):e54421, (2013)
~ 1-10 ns
~ 1-10 ps
1 GW/cm2
300 ps @ 80 Mhz, 𝜏 = 3 ns
200 MW/cm2
1.5 ns @ 80 Mhz, 𝜏 = 3 ns
100 MW/cm2
3 ns @ 80 Mhz, 𝜏 = 3 ns
Notes: However, the suppression of fluorescence can be fully recovered if the fluorescence is collect only after the action of all the stimulating photons (time-gating detection).
In essence, collecting fluorescence only after action of the STED pulse ensures that the signal stems from fluorophores that have resided into the excited-state at least for the time of the pulse, thus has been exposed to all stimulating photons.

## Slide 56: Gated Pulsed-STED (gP-STED)
56
ultra-fast laser architectures
(including OPO)
sub-nanosecond
fiber lasers
STED
time
detection
12.5 ns @ 80 Mhz
exc.
Castello, M.,…, Vicidomini, G., Micr. Res. Tech., 79(9):785-791, (2016)
complexity in the laser architecture reduces
800 ps, 𝜏 = 3 ns

## Slide 57: Gated Pulsed-STED (gP-STED)
57
ultra-fast laser architectures
(including OPO)
sub-nanosecond
fiber lasers
STED
time
detection
12.5 ns @ 80 Mhz
exc.
Castello, M.,…, Vicidomini, G., Micr. Res. Tech., 79(9):785-791, (2016)
800 ps, 𝜏 = 3 ns
complexity in the laser architecture reduces
without any resolution lost;

## Slide 58: Gated Pulsed-STED (gP-STED)
58
ultra-fast laser architectures
(including OPO)
sub-nanosecond
fiber lasers
STED
time
detection
12.5 ns @ 80 Mhz
exc.
Castello, M.,…, Vicidomini, G., Micr. Res. Tech., 79(9):785-791, (2016)
complexity in the laser architecture reduces
without any resolution lost;
photobleaching reduces
800 ps, 𝜏 = 3 ns

## Slide 59
gated-STED Microscopy (from “the lifetime tuning” perspective)

## Slide 60: Time-Resolved STED Principle
60
𝜏fl = 1/(kfl+kSTED) with kSTED ～ ISTED
S0
S1
Notes: The basic principle behind time-resolved STED is the fact that an excited molecule illuminated by a STED beam shorts it fluorescence lifetime, in essence if the molecule emits the fluorescent photon it is emitted immediately. Indeed, in presence of the STED beam the molecule has a new de-excitation pathway, whose rate is proportional to the intensity of the STED beam.

## Slide 61: Time-Resolved STED Principle
61
S0
S1
𝜏fl = 1/(kfl+kSTED) with kSTED ～ ISTED
Notes: Since the STED beam is shaped as a doughnut the lifetime of the molecule distributed within the effective excitation volume of the STED microscope is not uniform. In particular, molecule in the center of the donut will have a longer lifetime

## Slide 62: Gated (CW) STED Microscopy
62
S0
S1
Vicidomini G.,…, Hell S.W., Nat. Methods, 8(7): 571-573 (2011)

## Slide 63: Gated CW-STED Microscopy
63
Vicidomini G.,…, Hell S.W., Nat. Methods, 8(7): 571-573 (2011)

## Slide 64: Tune Resolution by Time (or Intensity)
64
Vicidomini G.,…, Diaspro A., Methods, 66 (2), 124-130 (2014)
d= 𝛌/(2*NA*√((1+ImSTED))*(1+Tg))
Signal ~ exp (-Tg/𝜏)
The resolution improves both with the increase of the STED beam intensity ImSTED and the time-delay Tg
but also the signal decreases, thus the SNR decrease with the increase of Tg

## Slide 65
Separation by Lifetime Tuning (SPLIT-) STED

## Slide 66: SPLIT-STED Principle
r (nm)
0
-200
+200
ISTED(r)
Iexc.(r)
F(r)
𝜏STED(r)
0
0
1
1
Intensity (a.u.)
Intensity (a.u.)
Lifetime (𝜏fl)
0
1
r
Lifetime (𝜏fl)
0
1
0
20
t (ns)
fSF(t,r = 0) (a.u.)
0
1
fluorescence signal of a single-fluorophore
with

## Slide 67: SPLIT-STED Principle
r (nm)
0
-200
+200
ISTED(r)
Iexc.(r)
F(r)
𝜏STED(r)
0
0
1
1
Intensity (a.u.)
Intensity (a.u.)
Lifetime (𝜏fl)
0
1
rout
Lifetime (𝜏fl)
0
1
0
20
t (ns)
F(t) (a.u.)
0
fluorescence signal from the detection volume (two fluorophores)
rin
1
fluorescence signal of a single-fluorophore
with

## Slide 68: SPLIT-STED Principle
r (nm)
0
-200
+200
ISTED(r)
Iexc.(r)
F(r)
𝜏STED(r)
0
0
1
1
Intensity (a.u.)
Intensity (a.u.)
Lifetime (𝜏fl)
0
1
rout
Lifetime (𝜏fl)
0
1
0
20
t (ns)
F(t) (a.u.)
0
fluorescence signal from the detection volume (two rings)
rin
1
fluorescence signal of a single-fluorophore
with

## Slide 69: SPLIT-STED Principle
r (nm)
0
-200
+200
ISTED(r)
Iexc.(r)
F(r)
𝜏STED(r)
0
0
1
1
Intensity (a.u.)
Intensity (a.u.)
Lifetime (𝜏fl)
0
1
rout
Lifetime (𝜏fl)
0
1
0
20
t (ns)
F(t) (a.u.)
0
rin
1
g
s
0
1
0.0
0.5
P
phasor plot representation
fluorescence signal from the detection volume (two rings)
fluorescence signal of a single-fluorophore
with
universal semicircle

## Slide 70: SPLIT-STED Principle
r (nm)
0
-200
+200
ISTED(r)
Iexc.(r)
F(r)
𝜏STED(r)
0
0
1
1
Intensity (a.u.)
Intensity (a.u.)
Lifetime (𝜏fl)
0
1
rout
Lifetime (𝜏fl)
0
1
0
20
t (ns)
F(t) (a.u.)
0
fluorescence signal of a single-fluorophore
with
fluorescence signal from the detection volume (two rings)
rin
1
phasor plot representation
g
s
0
1
0.0
0.5
P
Pout
Pin
universal semicircle

## Slide 71: SPLIT-STED Principle
r (nm)
0
-200
+200
ISTED(r)
Iexc.(r)
F(r)
𝜏STED(r)
0
0
1
1
Intensity (a.u.)
Intensity (a.u.)
Lifetime (𝜏fl)
0
1
rout
Lifetime (𝜏fl)
0
1
0
20
t (ns)
F(t) (a.u.)
0
rin
1
g
s
0
1
0.0
0.5
P
Pout
Pin
inner photons are obtained by simply inverting a linear system
fluorescence signal of a single-fluorophore
with
fluorescence signal from the detection volume (two rings)
phasor plot representation
universal semicircle

## Slide 72: SPLIT-STED Principle (& Background)
r (nm)
0
-200
+200
ISTED(r)
Iexc.(r)
F(r)
𝜏STED(r)
0
0
1
1
Intensity (a.u.)
Intensity (a.u.)
Lifetime (𝜏fl)
0
1
rout
Lifetime (𝜏fl)
0
1
0
20
t (ns)
F(t) (a.u.)
0
rin
1
g
s
0
1
0.0
0.5
P
Pout
Pin
inner photons are obtained by simply inverting a linear system
fluorescence signal of a single-fluorophore
with
fluorescence signal from the detection volume (two rings)
phasor plot representation
Pback
universal semicircle

## Slide 73: SPLIT-STED Implementation
g
s
0
1
0.0
0.5
P(x)
Pout
Pin
Pback
universal semicircle
Lanzanò L.,…, Vicidomini G., Nat. Comm., 6,6701 (2015)
universal semicircle
signal of fluorophores in the “zero” intensity point
signal of fluorophores at r equal to the doughnut crest

## Slide 74: SPLIT-STED
74
Confocal and STED measurements of fixed Hela cells, with Oregon-Green 488 - labelled tubulin.
Confocal
Lanzanò L.,…, Vicidomini G., Nat. Comm., 6,6701 (2015)

## Slide 75: SPLIT-STED
75
STED-FLIM
Confocal and STED measurements of fixed Hela cells, with Oregon-Green 488 - labelled tubulin.
Lanzanò L.,…, Vicidomini G., Nat. Comm., 6,6701 (2015)

## Slide 76: SPLIT- Vs Gated-STED
76
Confocal and STED measurements of fixed Hela cells, with Oregon-Green 488 - labelled tubulin.
Photons from the center
(slow components)
Photons from the periphery (fast components)
anti Stokes-shift background photons
(uncorrelated)
Lanzanò L.,…, Vicidomini G., Nat. Comm., 6,6701 (2015)

## Slide 77: SPLIT-pSTED

## Slide 78: Acknowledgements
78
Dr. Sami Koho
Researcher
Dr Simonluca Piazza
Post Doc
Giorgio Tortarolo
PhD Student
Dr Marco Castello
Post Doc
Marco Scotto
Senior Technician
Dr Eli Slenders
Post Doc
Alessandro Rossetta
PhD Student
We are hiring Ph.D. Students, PostDocs, and an electrical engineering technician
Prof. Alberto Diaspro
Prof. Colin Sheppard
Dr. Paolo Bianchini
Dr. Takahiro Deguchi
Dr. Luca Lanzanò
Dr. Luca Pesce Dr. Michele Oneto Simone Pelicci Dr. Ivan Coto Hernandez
Dr. Benjamin Harke Dr. Francesca Cella Dr. Silvia Galiani
Prof. Alberto Tosi
Dr. Federica Villa
Dr. Mauro Buttafava
Prof. Stefan W. Hell Dr. Andeas Schoenle Dr. Gael Moneron Dr. Haisen Ta
Prof. Kyu Young Han Dr. Volker Westphal Dr. Matthias Reuss Dr. Johann Engelhardt
Prof. Christian Eggeling